## Slide 1
Robot Operating System (ROS)
Autonomous Mobile Robots
NICOLA BEZZO, MASOUD BASHIRI
Fall 2016

## Slide 2
Autonomous Mobile Robots
100+ ROBOTS
100 SENSORS/ INTERFACES
2000+ LIBRARIES
http://www.ros.org
CODE REUSABILITY
ROS is a flexible framework for writing robot software

## Slide 4
What is ROS?
A meta Operating System for Robots. As an OS, provides:
  low-level device control
  implementation of commonly-used functionality
  message-passing between processes (they’re called nodes)
  package management
Tools and libraries for development and running code across machines
  Supports C++, Python and Lisp
    experimental libraries for Java
ROS is not an actual OS! it is a middleware. It sits on top of an OS (Linux and Mac are officially supported).
Autonomous Mobile Robots
UBUNTU
HARDWARE
ROS
App
App
App
App
IPC

## Slide 5
Controller Node
GPS Node
1) Advertise to GPS
4) Topic Request
5) Topic Stream
3) Host + Port
2) Subscribe to GPS
ROS Master
Operating System (Ubuntu 16.04)
ROS (Kinetic Kane)
CPU
SENSORS
ACTUATORS
2) Advertise to TWIST
1) Subscribe to TWIST
Motor
ROS Drivers
PUB/SUB ARCHITECTURE

## Slide 6
ROS Computation Graph
Master
  Provides name registration and look up to the nodes (Like a DNS Server).
Nodes
  Are executable that use ROS to communicate with other nodes.
  A ROS node is written with the use of a ROS client library, such as roscpp or rospy.
Messages
  A ROS message is a data structure, comprising typed fields. Nodes communicate with each other by passing messages. (Structures defined in .msg files)
Topics
  Each topic is a message bus that carries a certain type of message. Multiple nodes can subscribe and publish to a single topic. Also one node can subscribe and publish to many topics.
Autonomous Mobile Robots

## Slide 7
ROS Computation Graph (Cont’d)
Services
  ROS Services complements the subscriber/publisher communication model (Topics), by adding a synchronous request/reply model.
  A service provider node offers a service under a name and a client node uses the service by sending the request message and awaiting the reply.
Bags
  Bags are a format for saving and playing back ROS message data.
  Example: Storing sensor data to be used later.
Autonomous Mobile Robots

## Slide 8
Autonomous Mobile Robots
Master
Messages
Bags
Topics
Services
Nodes
Computation Graph

## Slide 9
Example: Topics
Asynchronous “Stream-like” Communication
TCP/IP or UDP Transport
Strongly typed (.msg files), supports primitive datatypes and arrays
Multiple Publishers
Multiple Subscribers
Autonomous Mobile Robots
credit: Clearpath Robotics

## Slide 10
Example: Services
Autonomous Mobile Robots
Synchronous “RPC-like” Communication
TCP/IP or UDP Transport
Strongly typed (.srv spec)
One Server
One or many clients
credit: Clearpath Robotics

## Slide 11
OPEN YOUR BOX
Autonomous Mobile Robots

## Slide 12
Rules
Your group number is the number that you find on the Turtlebot and computers that you have received.
Assign a name to your turtlebot: that’s your group’s name
Every time there is a Lab (usually on Thursdays) you (at least a member from your group) must pick up your robot from Rice 240 and bring it down to Rice 120. Viceversa, at the end of each class, you’ll have to bring the equipment back to Rice 240.
Please remember to charge your turtlebot and laptops before each lab session to avoid delays during the lab.
You are allowed to use only your assigned robot and computers (i.e., you cannot use other groups equipment)
Three dedicated networks are available to connect laptops and turtlebots. The networks SSID are AMR 1, 2, and 3. These networks are up and running in Rice 240. Please don’t remove the routers from the room.
You are allowed to use the equipment at any time during the semester.
The equipment can be used only inside Rice Hall, preferably inside/around Rice 240

## Slide 13
Communication
MASTER
SSH
2)
1)
Autonomous Mobile Robots
LENOVO
LENOVO
ACER
ACER

## Slide 14
Connect to your TurtleBot
Turn on your turtlebot laptop and connect to a network as follows
  1~3 connect to AMR1,
  4~6 connect to AMR2,
  7~10 connect to AMR3,
Turn on your workstation laptop (password=username) and connect to the same network
On the turtlebot laptop, open a terminal and type in ifconfig to find your IP. We will refer to this as IP_OF_TURTLEBOT
On the workstation laptop, open a terminal and type in ifconfig to find your IP. We will refer to this as IP_OF_PC
Autonomous Mobile Robots
network password is turtlebot

## Slide 15
Network Configuration
On the workstation Laptop (Lenovo)
  echo export ROS_MASTER_URI=http://IP_OF_TURTLEBOT:11311 >> ~/.bashrc
  echo export ROS_HOSTNAME=IP_OF_PC >> ~/.bashrc
On the Turtlebot Laptop (Acer)
  echo export ROS_MASTER_URI=http://localhost:11311 >> ~/.bashrc
  echo export ROS_HOSTNAME=IP_OF_TURTLEBOT >> ~/.bashrc
Verify the connection
  On the workstation Laptop, open a terminal and: rostopic list
  Do you see a list of topics? If not, verify that ROS_HOSTNAME is set properly on the turtlebot laptop
Autonomous Mobile Robots

## Slide 16
How to SSH into your Turtlebot
ssh turtlebot@[ip_of_turtlebot]
The password is 'turtlebot'
Now you have a secure shell connection to your acer laptop.
In the terminal type in: roslaunch turtlebot_bringup minimal.launch
  This roslaunch command runs a series of nodes in your turtlebot that allow you to get data from IMU, encoders, cliff sensors, bumper switches and send commands to the actuators
If you need another terminal connected to turtlebot you need to repeat the ssh procedure in a new terminal

## Slide 17
Please note that in the example below the username is 'ubuntu' whereas in your case it should be 'turtlebot'.

## Slide 18
Some Command-Line Tools
Autonomous Mobile Robots
Roscore
  Starts up ROS Master, ROS Parameter Server and RosOut logging node.
Rosbag
  Used for recording and playing data (from topics)
Rospack
  helps you find a package path. Usage: rospack find [package_name]
Roscd
  Allows you to cd directly to a package
  Also rosls shows the files and folders inside a package

## Slide 19
Some Command-Line Tools (Cont’d)
Autonomous Mobile Robots
rosrun
  allows you to run an executable in an arbitrary package.
roslaunch
  launches a set of nodes from an XML configuration file (.launch file) and includes support for launching on remote machines.
rostopic
  displays run-time information about topics and also lets you print out messages being sent to a topic.
rosparam
  enables getting and setting parameter server values from the command-line.

## Slide 20
Some Command-Line Tools - Graphical
Autonomous Mobile Robots
rqt_plot
  plots numerical data on a ROS topic over time.
rqt_graph
  displays an interactive graph of ROS nodes and topics.
rqt_bag
  is a graphical tool for viewing data in ROS bag files.

## Slide 21
Command tools: rostopic
rostopic echo [topic_name] //see the messages being publish in a specific topic
rostopic list //see a list of available topics
rostopic hz [topic_name] //see the rate of a topic
rostopic bw [topic_name] //see the bandwidth usage of a
topic

## Slide 22
Publish to a topic in command line
rostopic pub -r [rate] [topic_name] [msg] //publish to a topic
Example: Let's make the robot move by publishing a Twist
Message to the '/cmd_vel/input/navi' that specifies a linear
Velocity of 0.1(m/s), play around with the parameters and observe the behavior of turtlebot.
rostopic pub -r 10 /cmd_vel_mux/input/navi geometry_msgs/Twist '{linear: {x: 0.1,y: 0.0,z: 0.0},angular: {x: 0.0,y: 0.0,z: 0.0}}'

## Slide 23
Use rosbag and rqt_bag to record and playback/
plot topic data
First make a directory to save your bag files
mkdir ~/bagfiles
Now let's start recording a topic, for examle /odom
Rosbag record /odom
Hit ctrl+c to stop the recording process now use rqt_bag
To playback and plot the recorded data
rqt_bag [your_bag_file]

## Slide 24
Use rosbag and rqt_bag to record and playback/plot topic data

## Slide 25
Catkin Package Management Tool
Autonomous Mobile Robots
Catkin is a package management tool developed for ROS users that makes package management easier.
Let’s create a catkin workspace and our first package
Open a terminal

## Slide 26
Create a package and build a catkin workspace
cd ~/catkin_ws/src
catkin_create_pkg [package_name] dep1 dep 2 …
cd ~/catkin_ws/
catkin_make
Next step is sourcing the setup file
Source ~/catkin_ws/devel/setup.bash
Autonomous Mobile Robots

## Slide 27
#include "ros/ros.h"
#include <geometry_msgs/Twist.h>
#include <sensor_msgs/Imu.h>
void imuCallback(const sensor_msgs::Imu::ConstPtr& data)
{
ROS_INFO("Angular Velocity = %f", data->angular_velocity.z);//print out the angular velocity
}
int main(int argc, char **argv)
{
ros::init(argc, argv, "turtlebot_turn");
ros::NodeHandle nh;
ros::Publisher vel_pub;
vel_pub = nh.advertise<geometry_msgs::Twist>("/cmd_vel_mux/input/navi", 1, true);
ros::Subscriber sub = nh.subscribe("/mobile_base/sensors/imu_data", 10, imuCallback);
ros::Rate loop_rate(10);
int count = 0;
geometry_msgs::Twist vel;
vel.linear.x = 0;//linear velocity(m/s)
vel.angular.z = 1.0;//angular velocity(rad/s)
while (ros::ok())
{
vel_pub.publish(vel);
ros::spinOnce();
loop_rate.sleep();
++count;
if(count==20)
vel.angular.z = 0;
}
return 0;
}
Example Code: turtlebot_turn.cpp
Autonomous Mobile Robots

## Slide 28
Useful Links
Ros Wiki Turtlebot Page
Catkin Tutorial
The Turtlebot Stack on Github
Turtlebot Demos
UNIX Tutorial for Beginners
Turtlebot Guide and Support
Autonomous Mobile Robots